## Slide 1: Update on upconverter design, closed loop test & Firmware design (ALPACA)
July 2nd 2025
M. Naafs, P. Bos Nikhef contributors: M. Naafs (EE), P. Bos (EE), G. Visser (EE), M. Adams (ME), V. van Beveren (SWE), T. Damen (SWE), J. Mead (Phys), A.P. Colijn (Phys)

## Slide 2
RF readout: cryogenic amplifier & downconverter
Low noise amplifier

## Slide 3
Input range: ~ 25.5 to 27.5 GHz
Ouput centred at ~ 450 MHz
Expected signal power: -130 dBm to -120 dBm (0.1 fW to 1 fW)
Cryogenic amplifier gain: 28 dB (~630x)
Downconverter input: -102 dBm to -92 dBm
(0.1 pW to 1 pW)
Downconverter is currently in use at LNGS
Previously: cryogenic amplifier & downconverter
How weak of a signal is -120 dBm? -Receiving at earth, the light from a 100 W light bulb on the moon -Deep Space Network (DSN) uses 34 m dish antenna to receive -120 dBm (S-band) from James Webb Space Telescope (1.74 Gm away)

## Slide 4
Analogue – digital conversion done by Xilinx RF-SoC Ultrascale+
8x 5 GSPs ADCs
8x 10 GSPs DAC
Used to make FFTs and stream data to disk
FW made by Pascal Bos
Data readout & A/D conversion

## Slide 5
To make a “closed loop” test 
Inject a self-made test signal
Test detection algorithms
Why make one?
No really viable options are available for purchase on the market
Why do we need an upconverter?
Made at Nikhef
Previously made at Nikhef, now in use in Italy
Commercial unit
FPGA Dev-board + gaming PC

## Slide 6
Design is finished
Production quotes have been requested  will be ordered when quotes are in & chosen
Upconverter specs
Baseband input: DC – 6 GHz
IF Input: 800 MHz – 6 GHz
RF Output: 24 – 44 GHz
RF output power: ~3 dBm
Currently: Upconverter PCB

## Slide 7
Block schematic of the upconverter
7
Mixer
LO
(PLL)
Ref shaper
100 MHz in
LO aprox. 5 GHz.
0
180 Deg
Balun
I (0)
Q (90)
Low noise
Power supply
Internal
4 x lo
SPI
control
26.5 GHz
mm wave out
Controller
board
upconverter
RF SOC
DAC
Controller
board
 To attenuator

## Slide 8
Upconverter housing has been made
Next steps: -Send to company for coating -Order RF seals
Upconverter housing
Why put upconverter in a shielded box?
Radiated signal through air might swamp received signal on downconverter
Leaked signals might be O(20-60 dB) (~ 100x – 1E6x) stronger than att. signal

## Slide 9
For the downconverter a controller was made based on the Nikhef Embedded Platform (NEP), running Zephyr OS.
This will be reused for the upconverter
Controller PCB

## Slide 10
Upconverter produces ~ 3 dBm output power  we need -120 dBm
Making controlled attenuation is hard. It is cheaper to buy than to make yourself
We chose R&S RSC controllable step attenuator
The remainder of attenuation is done with up to 60 dB of inline coaxial 2.92 mm attenuators
Controllable attenuator
External attenuator (RSC-Z405): DC to 40 GHz, 5 dB steps, 0 – 75 dB

## Slide 11
Please switch from thinking analogue to digital now 
On to part II, Digital design & FW

## Slide 12
Digital design, status
What we are doing
Where we are now
Where we are going

## Slide 13
Digital design, status,
What is happening?
We are using a FPGA with integrated ADC’s to process the first signals originating from the electrons.
This is achieved by a using a 2D FFT engine, that allows lossless frequency domain transformations.
It’s called: “Advanced Lossless Processor for Analogue” Conversions and Analysis. Or ALPACA for short. (thx chatgpt)

## Slide 14
Digital design, status,
Inside Alpaca
ALPACA uses a 2D Fast Fourier Transform called “Bailey’s Algorithm”. Ideal for parallel processors and perfect for FPGA’s.
Currently we can perform 2^16 points FFT’s 13μs. Resulting in 76kHz of frequency resolution. Without throwing away a literal bit of information. (But we are Hann windowing, so some suppression is being done)
Better resolutions can be achieved by:
  Lowering sample rate (at the cost of bandwidth)
  Increase fft size (at the cost of refresh rate.)
Currently a basic trigger function is ready. By “box triggering”, this can be adjusted at run time and can be adjusted/expanded to our needs.

## Slide 15
Digital design, status,
Where is alpaca going?
Future development could focus on:
  Suppressing the weighting effect. Caused by windowing (high cost because of double implementation).
  Increasing frequency resolution.
  Integrating the RFSoC into test setup at LNGS (current priority).
Sources :https://gitlab.nikhef.nl/bosp/ptolemy_daq_design
Email: pascal.bos@nikhef.nl

## Slide 16
Downconverter in use @LNGS
Thank you for your attention
RFSoC for FW developemtent @Nikhef

## Slide 17
Backupslides

## Slide 18
“First Light”
Source (26.5GHz)
Downconverter
This not a proper measurement
Next Slide is proper
Source

## Slide 19
Upconverter housing – exploded view

## Slide 20
ALPACA backupslides

## Slide 21
Backup
Most of the signals don’t start at zero.
So the sinusoid here has a “step”.
This messes you up.
Windowing suppresses this step by multiplying it with near-zero.

## Slide 22
Backup,
Octave script to “proof” Baileys algorithm.
implementing this in a hdl, A LOT HARDER.

## Slide 23
Backup
Things made so far (by Pascal):
  HDL design
    Managing ADC’s & DAC’s data streams
    Ported ‘Wupper’ to RFSoC to use PCIe
    Wrote a lossless FFT implementation.
  Ported Linux on the CPU of the RFSoC
  Made a linux kernel driver to connect CPU<->FPGA
  Made userspace apps to manage RfSoC.
  Wrote C++ to visualize information, including data protocols.
Things to make:
  Document things more.
  Implement Bailey’s algorithm done
  Implement it twice to counter window suppression effects.